## Slide 1: Understanding pulsar data with PSRCHIVE
Daniel Reardon (Swinburne/OzGrav) Many slides from Andrew Zic, Ryan Shannon, and James McKee
Notes: Present how we have limits on GW levels to constrain the massive black hole population

## Slide 2: Motivation
Pulsars enable high precision astrophysics
  Gravitational waves
  General relativity
  Matter at extreme density
  Interstellar plasma, neutron star interior and magnetosphere, solar system and solar wind, stellar astrophysics, and more!
We want to do the bests tests possible
  Need the best telescopes
  Need the best instrumentation
  Need the best data sets and tools to analyze them
Q: What does the data look like?
A: Use PSRCHIVE to see!
Credit: David Champion
Schematic representation of Pulsar Timing Array
Telescope -> Receiver -> Backend -> Pulse profiles -> Time-tagging -> Timing residuals -> Physics

## Slide 3: Antennas: the “body”
Pulsars are faint
Large antenna size = large sensitivity
Historically: Large aperture single-dish telescopes
  Don’t need angular resolution
Now: Interferometers
  MeerKAT/LOFAR/VLA/SKA
Sites chosen for low radio-frequency inference
Works at observing frequencies of choice
MeerKAT, South Africa (credit: SARAO)
Greenbank, USA (credit: Jay Young)
FAST, China

## Slide 4: Receivers: the “heart”
"Frontend” – turns radio waves into electricity (voltages)
Choosing observing frequencies
  Pulsars are brighter at lower frequency
  The sky background is brighter at low frequency
  The ionized gas in the interstellar medium affects low frequencies.
  Precision pulsar timing is typically done between 600 MHz - 3 GHz (50 cm - 10 cm wavelengths)
System temperature
  Adds randomness, “noise”, to the data
  The lower the better
  Can’t build expensive cooling systems for large arrays
Murriyang/Parkes 10-50cm dual band receiver

## Slide 5: Backends: the “brains”
Digitize the electric signal (voltages)
  time series from the frontend
Data processing
  Channelization
  Dedispersion
  Phase binning
  Time sampling
Data types:
  Voltages -> Save everything and process later
  Search mode -> Channelized high time resolution
  Fold mode -> compact data cube for known pulsars. High time resolution in pulse phase
Pulses on first Australian $50 note

## Slide 6: Pulsar folding
Pulsars are faint
  For most pulsars observed with most telescopes, individual pulses are indistinguishable from the noise
  Average together many pulses to get a clearer signal
In pulsar timing, we are studying known pulsars
  We have a good model for the rotation of pulsar
Pulse period, P

## Slide 7: Pulsar folding
Pulsars are faint
  For most pulsars observed with most telescopes, individual pulses are indistinguishable from the noise
  Average together many pulses to get a clearer signal
In pulsar timing, we are studying known pulsars
  We have a good model for the rotation of pulsar

## Slide 8: Pulsar folding
Pulsars are faint
  For most pulsars observed with most telescopes, individual pulses are indistinguishable from the noise
  Average together many pulses to get a clearer signal
In pulsar timing, we are studying known pulsars
  We have a good model for the rotation of pulsar

## Slide 9: Fold mode data cube
One pulse profile per:
  Frequency channel
  Time sub-integration
  Polarization
PSRCHIVE lets us explore this fold-mode data hyper-cube.
  Archive files
CASPSR
PDFB4
frequency
time
polarisation
each point in slab is a pulse profile
psrchive is used to process these data

## Slide 10: Pulse profile
Dai et al. (2015)
Linear polarization position angle
White: total intensity
Red: linear polarization
Blue: circular polarization
Profiles can have microsecond time resolution

## Slide 11: What is PSRCHIVE?
A software suite, not a single monolithic program:
  Integrated with UNIX environment
  A C++ development library with python bindings
  Open-source
  Powerful
https://psrchive.sourceforge.net/index.shtml

## Slide 12: Resources for PSRCHIVE
https://psrchive.sourceforge.net/manuals
Bonus: IPTA student week 2024 tutorial:
https://github.com/andrewzic/IPTA_PSRCHIVE_tutorial_2024

## Slide 13: What can PSRCHIVE do?
Inspect (and edit) archive metadata (psredit, vap)

## Slide 14: What can PSRCHIVE do?
Compute statistics (psrstat, pdv)
Modify data products (psrsh, pam):
  Time, frequency, polarization averaging
  De-dispersion
Dispersed pulse as a function of frequency

## Slide 15: What can PSRCHIVE do?
Visualise data (psrplot, pav)
Profile vs frequency
Profile vs time
Profile polarisation

## Slide 16: Profiles with frequency
Physics!
  Dispersion
    Interstellar medium disperses radio waves
    Low frequencies arrive later than high
  Pulsar intrinsic spectrum
    Pulsars typically brighter at low frequency
  Pulse width changes
    High frequencies come from lower in the magnetosphere
  Scattering / scintillation
    Density fluctuations in the interstellar medium cause propagation and interference
Radio-frequency interference (RFI)

## Slide 17: Profiles with frequency
Physics!
  Dispersion
    Interstellar medium disperses radio waves
    Low frequencies arrive later than high
  Pulsar intrinsic spectrum
    Pulsars typically brighter at low frequency
  Pulse width changes
    High frequencies come from lower in the magnetosphere
  Scattering / scintillation
    Density fluctuations in the interstellar medium cause propagation and interference
Radio-frequency interference (RFI)

## Slide 18: Profiles with frequency
Another pulsar profile versus frequency
the effect of scattering
Channels removed because of interference

## Slide 19: Profiles with time
Physics!
  Scintillation
    Interference pattern moves as the Earth/pulsar/ interstellar medium move
  Mode changing
    The pulsar emission changes
  Jitter
    Random pulse shape and intensity variations make the brightness vary randomly
Bursts of RFI
Right: Parthasarathy et al. (2021)

## Slide 20: What can PSRCHIVE do?
Excise interference (paz, pazi)

## Slide 21: Radio-frequency interference
RFI is everywhere
Satellites, cell phone, wifi, planes, radio broadcast, lightning, microwaves
Above: Fraction of time a channel has been removed due to RFI at MeerKAT

## Slide 22: Radio-frequency interference in data
Narrow-band
Bursts

## Slide 23: What can PSRCHIVE do?
Calculate and correct for rotation measure (rmfit)

## Slide 24: What can PSRCHIVE do?
Polarization/flux calibrate observations (pac, pcm)

## Slide 25: What can PSRCHIVE do?
Calculate optimal period and DM of pulsar candidates (pdmp)

## Slide 26: What can PSRCHIVE do?
Combine multiple observations (psradd)
Form standard templates for timing (psrsmooth, paas)

## Slide 27: What can PSRCHIVE do?
Estimate times of arrival (pat)
  “time tagging”
  Shift the noise-free template in phase until it matches the data
Relative to timing model arrival times varied show excess white noise due to pulse jitter
Millisecond pulsars easily measured to less than 1 microsecond precision
TOA (MJD) 58186.821751361541342
Error (microsec) 0.029

## Slide 28: Saving times of arrival (ToAs)
Measured ToAs are saved to a text file (.tim file) with flags describing the observation
Pulsar timing data sets often have thousands of ToAs
File name
Frequency (MHz)
ToA (MJD)
Uncertainty (us)
Telescope
Flags

## Slide 29: Summary
The journey of pulsar timing data
Big radio telescopes in radio-quiet regions observe pulsars for minutes to hours
  Receivers transform radio waves to voltages
  A backend system folds data at the pulsar period and saves profiles as a function of frequency, time, and polarization
PSRCHIVE is used to
  Remove Radio-frequency interference (RFI)
  Calibrate observations
  Sum profiles in frequency, time, polarization
  Form templates profiles
  Time tag profiles with precise times of arrival (ToAs)
https://github.com/andrewzic/IPTA_PSRCHIVE_tutorial_2024
Timing residuals are then analyzed for interesting physics missing in the model
  Gravitational waves!

## Slide 30: Bonus: Software to use
Voltages processed (e.g. folded) with dspsr
Search mode searched for new pulsars with presto
Pulse profiles calibrated and analysed with psrchive
Timing residuals and (least squares) timing model fit in tempo2 or PINT
Stochastic (random) processes, and timing model fit with Bayesian inference with temponest or enterprise
Gravitational wave detection enterprise and discovery

## Slide 31: Time tagging
Match a template to the pulse profile observation
  Shift the template in phase until it best matches the data
Relative to timing model arrival times varied show excess white noise
Millisecond pulsars easily measured to less than 1 microsecond

## Slide 32: Time tagging
Match a template to the pulse profile observation
  Shift the template in phase until it best matches the data
Relative to timing model arrival times varied show excess white noise
Millisecond pulsars easily measured to less than 1 microsecond

## Slide 33: ToA uncertainty
What properties of telescope/receiver/pulsar give the best ToAs?
Best millisecond pulsars can be time-tagged to 10 nanoseconds uncertainty!
However, measurements often show excess noise
Jitter noise in J1603-7202 (Parthasarathy et al. 2021)

## Slide 34: Timing residuals
A model is used to predict the arrival times
The model is developed following the discovery of a pulsar
It is always improving with more data collected
Timing residuals = ToAs – model
  Timing residuals reveal physics missing from the model.

## Slide 35: Noisy timing residuals
Observations of millisecond pulsar B1937+21
Last observation (2018): 674,489,762,880 pulse periods after first observation (1984)
Spin noise
Dispersion measure variations in PSR J0437-4715

## Slide 36: The timing model
Text file of parameters and uncertainties (.par file)
Pulsar spin
Astrometry (position, motion)
Dispersion
Keplerian binary orbit
Post-Kelperian effects (geometric, relativistic)
Solar wind / solar system
Instrumental offsets

## Slide 37: More profiles
Average over time and frequency
Pulsars have different shapes
  Depends on spin properties of pulsars
  Depends on viewing angle of pulsar beam
  Depends on shape of emission region
  Narrow pulses provide higher timing precision
Example: MeerKAT profiles of millisecond and recycled pulsars
Spiewak et al. (2022)